## Slide 1: VA Mobility Screening and Solutions Tool (VAMSST) Training for NON-Acute Care Areas
VHA Safe Patient Handling and Mobility VHASPHM@va.gov

## Slide 2: History and Background
SPHM leaders identified the need for a mobility screening tool that could be used by all healthcare and lay persons to screen mobility for appropriate equipment selection to keep everyone safe.
The VHA Nursing Innovations Center for Evaluation (NICE) accepted the quality improvement project to develop a new tool, using BMAT as a framework.
The VA MSST is the product of this 2-year interdisciplinary QI project and is validated and approved for use internal to VHA until published to the public.
VA MSST inter-rater reliability was excellent and statistically significant across all caregivers (both licensed and unlicensed).
As a result, we are working toward switching to VA MSST for screening mobility status.
VA MSST is being used to promote a culture of early and progressive mobility to inform the safest way to mobilize patients no matter their location/care environment.

## Slide 6: Using the Tool
Use VA MSST with every mobility encounter to ensure patient and staff safety. This includes all care areas (e.g. acute care, CLC, therapy, imaging, dental, HBPC, ED, etc).
Always default to the safest choice for equipment. Consider factors that may affect screening (e.g. patient’s ability to follow commands, sleep deprivation, low O2, medications, orthostatic hypotension, hypoglycemia, hypovolemia).
Remember if the answer to the 1st question is “yes”, follow blue line to Level 4.
Document level in local notes per facility policy/decision.

## Slide 7: Patient Education
Your safety is our important concern. In order to keep you and us safe, we will screen your mobility every time we go to get you up.
This helps us decide the most appropriate equipment to use, so that we can safely mobilize you.
Safe mobility keeps you doing the things you want to do.

## Slide 9
If the patient is unable to sit up independently, they require total assistance/VA MSST Level 1. This means they need help with sitting up, standing and walking.
It does NOT mean they CANNOT sit up, stand up or walk. It means they need a mechanical lift to assist them for their own safety and for the caregiver safety.
You will see that a total assistance patient can use an ambulation harness or other appropriate equipment. Imagine a patient who had a total knee replacement yesterday and needs to walk but is just a little unsteady and needs a steadying hand to sit up.
VA MSST LEVEL 1: TOTAL ASSIST
Copyright EarlyMobility.com, 2019. All rights reserved. Used with permission by Veterans Administration Healthcare System. EMOBI used with permission from EarlyMobility.com. INTERNAL VA USE ONLY

## Slide 10
Your patient is groggy from receiving medications in Emergency Department. They are extremely weak and cannot even begin to sit up by themselves.
  They may be able to sit with assistance of a seated sling.
  They will require total assistance.
  VA MSST Level 1.
Your patient in CLC has pneumonia and was walking yesterday but they feel lousy because they were allergic to the antibiotic given. They are dizzy at the edge of the bed. You do not feel it is safe to let them sit by themselves.
  They should be walking today but need a device in case of dizziness or falling.
  They require total assistance.
  VA MSST level 1.
Your patient has been placed on strict bedrest orders.
  They require total assistance and should not get out of bed.
VA MSST LEVEL 1: TOTAL ASSIST
Copyright EarlyMobility.com, 2019. All rights reserved. Used with permission by Veterans Administration Healthcare System. EMOBI used with permission from EarlyMobility.com. INTERNAL VA USE ONLY

## Slide 11
If the patient CAN sit up independently, the next question is if they have the strength to try and stand up.
The Stretch and Point step is a very important step which is why it has its own whole category in the screen.
Traditionally, staff would try to have a patient stand up without doing this step and many staff injuries and falls occur with patient knees buckling.
If they are unable to stretch at least one leg to almost straight and point their toes, they are moderate assistance, level 2.
This means they require power to even try and stand up because they lack the strength in their legs to safely try to stand without a device.
It does NOT mean they CANNOT stand up or walk. It means they need a mechanical lift to assist them for their own safety and for caregiver safety.
VA MSST LEVEL 2: MODERATE ASSIST
Copyright EarlyMobility.com, 2019. All rights reserved. Used with permission by Veterans Administration Healthcare System. EMOBI used with permission from EarlyMobility.com. INTERNAL VA USE ONLY

## Slide 12
If the patient CAN sit up independently and has the strength and movement in at least one leg to try and stand up, the next question is to see if they can stand safely on their own.
If they are unable to clear their buttocks, you know they need power to stand.
The patient will be VA MSST level 3P/moderate assistance to stand.
Many have asked why not just combine level 2 and level 3P. The reason for this is that this would result in the stretch and point being skipped over.
The patient must be able to stretch and point AND stand without losing balance to pass to the 3N (minimal assist category) and BOTH level 2 and level 3P require moderate assist to stand and walk (power) but a level 2 lacks leg strength, a level 3P can try to stand but lacks glute strength to clear buttocks.
The Stretch and Point step is a very important step which is why it has its own whole category in the screen.
VA MSST LEVEL 3P (POWERED): MODERATE ASSIST
Copyright EarlyMobility.com, 2019. All rights reserved. Used with permission by Veterans Administration Healthcare System. EMOBI used with permission from EarlyMobility.com. INTERNAL VA USE ONLY
Notes: The goal is to keep everyone safe. There may be sometimes where the patient can clear their buttocks and stand but are a little unsteady. In this case the patient should have power to keep them safe.
Remember that the MSST is for ALL disciplines, including unlicensed staff to ensure everyone is safe. If it was designed for one discipline only, it would have looked different. There may be sometimes when this patient may not be using power, but the intent of the tool is to keep all safe and if in doubt, defaulting to power keeps everyone safe.

## Slide 13
If the patient CAN sit up independently, has good leg strength and is able to clear their buttocks from the surface to stand without loss of balance for 5 seconds, with or without an assistive device, the next question is whether they can safely walk.
If they are unable to pick up their feet to march in place and take steps forward and back with each foot, they are VA MSST Level 3N/minimum assist.
Remember if they cannot stand safely without loss of balance for 5 seconds, they remain a level 3P.
Level 3N patients need non-powered stand aid for mobility/locomotion but might use walker for stand up/simple transfer.
VA MSST LEVEL 3N (NON-POWERED): MINIMAL ASSIST
Copyright EarlyMobility.com, 2019. All rights reserved. Used with permission by Veterans Administration Healthcare System. EMOBI used with permission from EarlyMobility.com. INTERNAL VA USE ONLY
Notes: Remember that the MSST is for ALL disciplines, including unlicensed staff to ensure everyone is safe. If it was designed for one discipline only, it would have looked different. There may be sometimes when this patient may not be using power, but the intent of the tool is to keep all safe and if in doubt, defaulting to power keeps everyone safe.

## Slide 14
If the patient can march in place and step forward and back safely using adaptive device but not without device, they are independent with adaptive device so VA MSST Level 4A/ independent.
If patient is independent with wheelchair, they are also VA MSST Level 4A/independent.
There may be some instances in structured rehabilitation such as working on balance or high-level gait activities where therapists may use ambulation harnesses or equipment to push activities.
Supervision needed if high fall risk.
VA MSST LEVEL 4A (ADAPTIVE) : INDEPENDENT
Copyright EarlyMobility.com, 2019. All rights reserved. Used with permission by Veterans Administration Healthcare System. EMOBI used with permission from EarlyMobility.com. INTERNAL VA USE ONLY

## Slide 15
If the patient can march in place and step forward and back safely without an adaptive device, they are VA MSST Level 4/independent.
Supervision needed if high fall risk.
VA MSST LEVEL 4: INDEPENDENT
Copyright EarlyMobility.com, 2019. All rights reserved. Used with permission by Veterans Administration Healthcare System. EMOBI used with permission from EarlyMobility.com. INTERNAL VA USE ONLY

## Slide 17: Video Resources
Introduction to MSST YouTube link: https://youtu.be/I9PPs2SB7zU
Scenarios that were used for the testing:
https://www.youtube.com/watch?v=wVcRbeWv-rQ